## Slide 1: Security Analysis and Improvements on WLANs
Giuseppe Miraglia
University of Pisa
15/07/2015
Li Wang, Bala Srinivasan, Nandita Bhattacharjee
Clayton School of IT, Melbourne, Australia

## Slide 2: IEEE 802.11 WLANs overview
WLAN: Wireless Local Area Network
IEEE or "I triple E", Institute of Electrical and Electronics Engineers: association of professionals in Electronics, Computer Engineering, Computer Science, etc.
IEEE 802.11: set of standards for WLANs created and mantained by IEEE (e.g. 802.11 b/a/g/n/ac etc., different Ghz & Mbps ranges)
Wi-Fi: “any WLAN product based on IEEE 802.11 standards”, often used as synonym for WLAN (majority of modern WLANs are based on these standards)
IEEE 802.11i: standard for security specifications of IEEE 802.11 series WLANs, replacement of old WEP (Wired Equivalent Privacy) standard

## Slide 3
known as WPA2 (Wi-Fi Protected Access 2)
aims to eliminate all known attacks against WEP …
… but provides solutions only to Confidentiality and Integrity, but not to some Availability aspects (e.g. DoS - Denial of Service attacks)
WPA before proposed as intermediate protocol between WEP and WPA2: less expensive, but less secure than WPA2
IEEE 802.11i security standard
Paper’s goal: propose solutions to improve security of IEEE 802.11i preventing attacks to it
"CIA" Triad

## Slide 4
Network Discovery
---
---
---
---
IEEE 802.11i security steps (1/5)
Beacon Frames
Probe Requests
APs broadcast beacon frames to announce their presence
Cs scan beacon frames to update their own list of reachable APs
Cs broadcast probe requests in order to find APs
APs answer with probe response
C1
AP1
C3
C2
C4
C1
C2
AP1
AP2
AP3
AP2
Notes: beacon == faro
probe == indagine

## Slide 5
both beacon frames and probe requests are sent in clear text  passive (listen but not alter) or active (listen and alter) eavesdropping attacks can be mounted
e.g. using active eavesdropping, a MiM can answer to probe requests and induce C to connect to him  information stealing
IEEE 802.11w standard for management frames resolves these issues, otherwise no improvements w.r.t. WEP
IEEE 802.11i security steps (1/5) – security
Network Discovery
---
---
---
---
Existing vulnerabilities:
Notes: Eavesdropping == intercettazione

## Slide 6
IEEE 802.11i security steps (2/5)
Two possible approaches in 802.11i:
PSK (Pre-Shared Key)
  firstly developed for WEP, maintained for backward compatibility
  widely used in home/small offices/ad-hoc WLANs: simple, economic and easy configurable
  known as WPA-PSK or WPA-Personal
  susceptible to offline-dictionary and internal attacks (see after 4-way handshake)
Open System
  "rough" link-layer authentication and association, no data encryption used  existing vulnerabilities as in step 1
  usually combined with 802.1x upper-layer authentication (next step)  in that case known as WPA-Enterprise
Network Discovery
IEEE 802.11 Authentication & Association
---
---
---

## Slide 7
IEEE 802.11i security steps (2/5) – cont.
PSK-based authentication
Network Discovery
IEEE 802.11 Authentication & Association
---
---
---
Authentication Response
(with plain-text challenge)
Authentication Request
Authentication Response
(with PSK-encrypted challenge)
Authentication Response
(SUCCESS / FAILURE)
Verify
challenge
using PSK
Generate
challenge
Encrypt
challenge
using PSK
C
AP

## Slide 8
Network Discovery
IEEE 802.11 Authentication & Association
---
---
---
IEEE 802.11i security steps (2/5) – cont.
Open System Authentication
A client C chooses an access point AP and starts the link-layer authentication process
(C status = "not authenticated, not associated")
link-layer 802.11 authentication request frame
(MACC + MACAP+ request + etc.)
C
AP
link-layer 802.11 authentication response frame
(MACAP+ MACC + SUCCESS / FAILURE + etc.)

## Slide 9
Network Discovery
IEEE 802.11 Authentication & Association
---
---
---
IEEE 802.11i security steps (2/5) – cont.
Open System Association
If the answer is SUCCESS, then C starts the link-layer association process with AP (C status = "authenticated, not yet associated")
link-layer 802.11 association request frame
(MACC + MACAP+ request + etc.)
C
AP
link-layer 802.11 association response frame
(MACAP+ MACC + SUCCESS / FAILURE + etc.)
If the answer is SUCCESS, then C is authenticated and associated to AP (C status = "authenticated, associated")

## Slide 10: IEEE 802.1x – based upper-layer authentication
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
---
---
IEEE 802.11i security steps (3/5)
when combined with Open System, known as WPA-Enterprise (skipped in WPA-Personal)
strong security and mutual authentication w.r.t. PSK-mode, but more expensive
requires an AP and a RADIUS Authentication Server (AS)
RADIUS (Remote Authentication Dial-In User Service): AAA (Authentication-Authorization-Accounting) protocol today standard de-facto for remote authentication
All C, AP and AS must support EAPOL (EAP Over LAN) incapsulation
EAP (Extensible Authentication Protocol): it does not defines itself an authentication protocol, instead it provides methods to negotiate "On the fly" the authentication method to use during the session (i.e. EAP-MD5, EAP-TLS, EAP-AKA, LEAP, PEAP, etc.)

## Slide 11
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
---
---
IEEE 802.11i security steps (3/5) - cont
C
AP
AS
Enterprise
Network
EAPOL Start auth.
EAP request UserID
EAP answer UserID
RADIUS access request for UserID
AS-side EAP-TLS
C-side EAP-TLS
RADIUS answer "SUCCESS" (with MSK)
MSK
MSK
PMK
PMK
Move PMK
PMK
PMK = PSK in
PSK-based authentication
Authentication Method Handshake
(es. EAP-TLS)
EAP Success

## Slide 12
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
---
---
IEEE 802.11i security steps (3/5) – security
PMK (Pairwise Master Key) derived from MSK (Master Session Key) and "fresh" (current session)
MSK exchanged with security during EAP-TLS session
EAP-TLS use a TLS (Transport Layer Security) session within EAP providing strong security:
  provides mutual authentication
  both C and AS own a certificate, so a PKI (Public Key Infrastructure) for validation is needed  more expensive
As alternative use EAP-MD5, but:
  only client-side authentication  possible MiM attacks to impersonate AP or AS  steal sensitive C’s data
  hash MD5-based  susceptible to offline-dictionary attacks
  cheap w.r.t. EAP-TLS, but less secure

## Slide 13: 4-Way Handshake
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
4-Way/Group Key Handshake
---
IEEE 802.11i security steps (4/5)
C
AP
PMK
PMK
Msg1 = { MACAP + NonceAP + SN }
Compute
NonceAP
Compute
NonceC
& PTK,
store PTK
Msg2 = { MACc + Noncec + SN + MICPTK(Noncec , SN) }
Compute
& store PTK,
verify MIC
Msg3 = { MACAP + NonceAP + SN+1 + MICPTK(NonceAP , SN+1) }
("Ready to use" )
Verify MIC
&
Install PTK
Verify MIC
&
Install PTK
Msg4 = { MACAP + NonceAP + SN+1 + MICPTK(NonceAP , SN+1) }
("OK, use" )

## Slide 14
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
4-Way/Group Key Handshake
---
IEEE 802.11i security steps (4/5) – cont.
NonceC and NonceAP are pseudo-random "number used once" used to avoid replay attacks and to generate PTK
PTK (Pairwise Transient Key) is build using the formula:
  where PRFn is a n-bit Pseudo Random Function
MIC (Message Integrity Code) is used to verify integrity and authenticity (similar to checksums) of a message msg:
let sent from A to B, with and k a key used to compute the MIC.
When B receives msg, it performs the check to check the integrity and authenticity of msg

## Slide 15: 4-Way Handshake DoS: msg1 in clear-text (v1)
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
4-Way/Group Key Handshake
---
IEEE 802.11i security steps (4/5) – security
C
AP
PMK
PMK
Compute
NonceAP
Msg2’ = { MACc + Noncec ’ + SN + MICPTK’(Noncec ’, SN) }
Msg1 = { MACAP + NonceAP + SN }
Compute
NonceMiM
Msg1’ = { MACAP + NonceMiM + SN }
Compute
NonceC
& PTK,
store PTK
Compute
NonceC‘
& PTK’,
store PTK’
(replace PTK)
Compute PTK,
verify MIC: Failure 
De-auth. client
MiM

## Slide 16: 4-Way Handshake DoS: msg1 in clear-text (v2)
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
4-Way/Group Key Handshake
---
IEEE 802.11i security steps (4/5) – security (cont.)
C
AP
PMK
PMK
Compute
NonceAP
Msg2 = { MACc + Noncec + SN + MICPTK(Noncec , SN) }
Msg3 = { MACAP + NonceAP + SN+1 + MICPTK(NonceAP , SN+1) }
Msg1 = { MACAP + NonceAP + SN }
Compute
NonceMiM
Msg1’ = { MACAP + NonceMiM + SN }
Compute
NonceC
& PTK,
store PTK
Compute
NonceC‘
& PTK’,
store PTK’
(replace PTK)
Verify MIC:
Failure - Discard
(4-way blocked)
Time-out 
De-auth. client
Compute
& store PTK,
verify MIC
MiM

## Slide 17: SOLUTION A
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
4-Way/Group Key Handshake
---
IEEE 802.11i security steps (4/5) – security (cont.)
C stores all PTKs and NonceAPs received in msg1s (no replacement)  when C receives msg3 from AP, it verifies the MIC using all PTKs
Consider 4-way handshake DoS attacks v2 (similar for v1)
PROBLEM OF SOLUTION A
Memory/CPU DoS attacks can be mounted: if flooding of msg1’ are sent by MiM , C easily fill its memory and loops on PTKs and NonceCs computation  again C de-authentication

## Slide 18: SOLUTION B: security on msg1
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
4-Way/Group Key Handshake
---
IEEE 802.11i security steps (4/5) – security (cont.)
C
AP
PMK
PMK
Msg1 = { MACAP + NonceAP + SN + MICPMK(Noncec , SN)}
Compute
NonceAP
Verify MIC &
Compute
NonceC & PTK,
store PTK
Msg2 = { MACc + Noncec + SN + MICPTK(Noncec , SN) }
Compute
& store PTK,
verify MIC
Msg3 = { MACAP + NonceAP + SN+1 + MICPTK(NonceAP , SN+1) }
Verify MIC
&
Install PTK
Verify MIC
&
Install PTK
Msg4 = { MACAP + NonceAP + SN+1 + MICPTK(NonceAP , SN+1) }
Use PMK as symmetric key (MiM can’t forge valid Msg1’ without PMK)

## Slide 19: SOLUTION C: NonceC reuse
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
4-Way/Group Key Handshake
---
IEEE 802.11i security steps (4/5) – security (cont.)
C
AP
PMK
PMK
Msg1 = { MACAP + NonceAP + SN }
Compute
NonceAP
Compute
NonceC & PTK,
store NonceC
Don’t store PTK
Msg2 = { MACc + Noncec + SN + MICPTK(Noncec , SN) }
Compute
& store PTK,
verify MIC
Msg3 = { MACAP + NonceAP + SN+1 + MICPTK(NonceAP , SN+1) }
Verify MIC &
Re-compute PTK
Using NonceC &
Install PTK
Verify MIC &
Install PTK
Msg4 = { MACAP + NonceAP + SN+1 + MICPTK(NonceAP , SN+1) }
Does not update NonceC when receives msg1’, until receives msg3
Memory DoS avoided
CPU DoS remains beacause PTK and MIC computed twice

## Slide 20: SOLUTION D: 3-Way Handshake
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
4-Way/Group Key Handshake
---
IEEE 802.11i security steps (4/5) – security (cont.)
C
AP
PMK
PMK
Msg1 = { MACAP + NonceAP + SN }
Compute
NonceAP
Compute
NonceC & PTK,
store PTK &
NonceC
Msg2 = { MACc + Noncec + NonceAP + SN +
MICPTK(Noncec , NonceAP ,SN) }
Verify NonceAP , Compute
& store PTK,
verify MIC

Install PTK
Msg3 = { MACAP + NonceC + SN+1 + MICPTK(NonceC , SN+1) }
Verify NonceC &
MIC, Install PTK
New formula prevent DoS (see next)

## Slide 21
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
4-Way/Group Key Handshake
---
IEEE 802.11i security steps (4/5) – security (cont.)
Observations on SOLUTION D (3-way handshake)
4-way  3-way beacause AP verifies authenticity and integrity after receiving msg2 (redundant msg4)
Memory DoS avoided: both C and AP store only their own Nonces and a PTK
CPU DoS avoided for AP: protected by MIC & NonceAP
CPU DoS avoided for C if the formula to compute PTK becomes:
  where PRFn is a n-bit Pseudo Random Function
   C can computes PTK in advance

## Slide 22: 4-Way Handshake with GTK (Group Transient Key)
Network Discovery
IEEE 802.11 Authentication & Association
IEEE 802.1x Authentication
4-Way/Group Key Handshake
---
IEEE 802.11i security steps (4/5) – cont.
C
AP
PMK
PMK
Msg1 = { MACAP + NonceAP + SN }
Compute
NonceAP
Compute
NonceC
& PTK,
store PTK
Msg2 = { MACc + Noncec + SN + MICPTK(Noncec , SN) }
Compute
& store PTK
& GTK (if 1°),
verify MIC
Msg3 = { MACAP + NonceAP + SN+1 + encrPTK(GTK) +
MICPTK(NonceAP , SN+1, encrPTK(GTK)) }
("Ready to use" )
Verify MIC
&
Install PTK
& GTK
Verify MIC
&
Install PTK
& GTK (if 1°)
Msg4 = { MACAP + NonceAP + SN+1 + MICPTK(NonceAP , SN+1) }
("OK, use" )

## Slide 23
Network Discovery
Secure Data Communication
4-Way/Group Key Handshake
IEEE 802.1x Authentication
IEEE 802.11 Authentication & Association
IEEE 802.11i security steps (5/5)
Once installed "fresh" PTK and GTK a secure channel of data communication over connected WLAN is established:
C can use PTK to encrypt unicast data frames
C can use GTK to encrypt multicast/broadcast data frames
 passive/active eavesdropping, modification etc. are no longer threats for transmitted data

## Slide 24
PSK-based authentication vulnerabilities
Offline dictionary attacks for passphrases:
Eavesdrop SSIDAP, MACAP, MACC, NonceAP and NonceC from 4-way handshake
Perform offline dictionary attack trying to derive passphrase:
where PBKDF2 (Password-Based Key Derivation Function 2) is a function that derives a 256 bit PSK applying 4096 times an hash function to the input.
Use as PMK to compute with the classic formula
Eavesdrop messages containing MICPTK and use to verify the MIC:
  If the check is correct, the searched passphrase
  Otherwise, return to step 2 and try with a different dictionary word
the attack can be mounted for passphrase of length <= 20
(8-63 admitted in WPA2-PSK) and that no contains special characters

## Slide 25
PSK-based authentication vulnerabilities - cont.
Man-in-the-Middle attacks for WLAN passive traffic monitoring:
From the internal or after a successful offline-dictionary attack, an adversary get not only the passphrase, but also PTK:
the correct passphrase give us the correct WLAN’s PSK (apply PBKDF2)
In PSK-based authentication, PSK is used as PMK during the 4-way handshake
PTK can be easily derived from PSK (PMK) using the classic formula
since PSK is unique over the same WPA-Personal WLAN, obtaining PTK for an user means obtaining PTKs of all users of WLAN only looking for their nonces!
 All the traffic of the clients connected to WLAN can be passively monitored by an adversary without traces

## Slide 26
ECC (Elliptical Curve Cryptography): public key cryptography based on algebraic structure of elliptic curves over finite fields
  strenght relies on intractability of ECDLP (Elliptical Curve Discrete Logaritmic Problem): let and points of an elliptic curve s.t. , is NPH to generate knowing and
  w.r.t. others public key cryptographies based on intractability of integers factorization (like RSA), ECC uses small keys (in #of bits) to provides the same security level
PSK-based authentication vulnerabilities: solutions
To prevent offline-dictionary and MiM attacks, PSK cannot be used directly as PMK  use of ECC-based ECDH protocol + PSK to derive PMK
Cypher Alg. | Key-length | RSA-keysize | ECC- keysize
3DES | 112 | 2048 | 224
AES | 128 | 3072 | 256
AES | 192 | 7680 | 384
e.g. to protect 128-bit AES keys, recc. key-size is:
3072 bits, if use RSA (exp. Increases)
256 bits, if use ECC (lin. increases)

## Slide 27
ECDH (Elliptical Curve Diffie-Hellman) protocol: key-exchange protocol that uses ECC for keys derivation
PSK-based authentication vulnerabilities: solutions
C
PSK
Choose dAP & compute dAP G
Choose dC,
compute dC G &
TPMK = dC dAP G
& hash
Verify hash
& assign
PMK = dC dAP G
(p, a, b, G, n, h)
AP
Å
dAP G
PSK
Å
dAP G, PSK
Å
dC G,
H(dC dAP G
, PSK
Å
dAP G, PSK
Å
dC G)
PSK
Å
dAP G,
H(dC dAP G
, PSK
Å
dAP G)
PSK
Å
dC G,
H(dC dAP G
, PSK
Å
dC G)
Verify hash &
install
PMK = dC dAP G
Verify hash &
Install PMK
p = ellipse field
a,b = curve coefficients
G = curve base-point
h: G’s cofactor
n: G’s order
dC , dAP secret keys
dAP G, dC G, public keys
Then perform handshake
To prevent offline-dictionary and MiM attacks, PSK cannot be used directly as PMK  use of ECC-based ECDH protocol + PSK to derive PMK

## Slide 28
External adversary doesn’t known PSK  unable to read encrypted traffic
Internal adversary known PSK, so it can sniff and decrypt traffic, but there’s no way to know secret keys (dC , dAP) knowing public keys (dAP G, dC G) thanks to the intractability of ECDLP
Security of ECDH + PSK
Offline-dictionary attacks avoided:
MiM attacks partially avoided:
External adversary doesn’t known PSK  unable to read encrypted traffic
Internal adversary known PSK, so it can forge messages like PSK Å dMiM G
 Internal MiM attacks for ECDH are still an unresolved issue

## Slide 29
Crucial 802.11i vulnerabilities are in 4-way handshake and in PSK-mode
valid solutions for 4-way hanshake are:
  check msg1 authenticity and integrity using MIC and PMK
  reuse the client-nonce
  use the 3-way handshake instead of the 4-way handshake
valid solutions in PSK-mode are:
  use "strong" passwords (length >= 20 and containing special characters)
  use ECC-based ECDH protocol to generate PMK, combined with PSK to encrypt the traffic
Conclusions